## Slide 1: Deep Reinforcement Learning for Simultaneous Sensing and Channel Access in Cognitive Networks

## Slide 2: Introduction
Rapid growth in wireless communication demands better spectrum utilization.
Dynamic Spectrum Access (DSA) allows opportunistic use of channels by Secondary Users (SUs).
Challenges arise due to partial observations and unknown PU behavior.
The proposed DDQSA framework is the first DRL method to jointly optimize sensing and access policies under partial observabilities.

## Slide 3: Problem Statement
Goal: Maximize long-term SU throughput in a POMDP environment.
Constraints: Narrowband sensing, time-slotted TDMA, PU traffic follow finite memory Markov chains and also no prior knowledge of PU transition probabilities.
Solution requires optimizing both sensing and channel access policies.Requiring intelligent trade-off btw exploration and exploitation.

## Slide 4: DDQSA: Double Deep Q-Network for Sensing and Access
Jointly learns sensing and access policies.
Optimizes long-term reward via DDQN training.
DDQSA learns which channels are worth sensing/accessing and gradually builds a robust policy by:
Reducing overestimation (Double DQN)
Focusing on important inputs (Selective Attention)
-Selective attention mechanism learns which channels to focus on based on past observations
Exploring wisely (ε-greedy + attention)
-With probability (ε):explore ;With probability (1−ε):exploit
Learning stably (Replay + target networks)

## Slide 5: Unified Policy Formulation
Observation space: history of sensed channel states.
Action space Aex: pairs sensing subset and access channel.
One-to-one mapping enables single-agent training.
Enables coordinated learning of sensing and access.

## Slide 6: System Model
Network with N channels, Kp PUs, and 1 SU.
PU traffic: Markov chain-based frame lengths.
SU senses L channels, decides access in the next slot.
Feedback: ACK (success) or NACK (collision).
- +1 for successful transmission (ACK), 0 or -1 for collision(NACK)

## Slide 7: DDQSA Workflow
1. Observe history vector oH(t).
2. Select joint action (sensing + access) using ε-greedy policy.
3. Execute actions, receive reward, update replay buffer.
- Store past transitions in sample mini-batches and update network via DDQN.
4.It receives feedback (ACK or NACK), which becomes the reward.
5.The DQN updates its internal Q-function based on this interaction.
6.Over time, the SU learns intelligent policies for maximizing throughput while avoiding interference
.

## Slide 8: Mathematical Framework
The goal is to find a policy π that maximizes the expected discounted reward:
π* = argmax_π Eπ [ Σ γ^t R(t) ]
The Q-value update rule is:
Q(s, a) ← Q(s, a) + α (r + γ max_a' Q(s', a') - Q(s, a))
DDQSA handles sensing and access jointly by encoding them in an extended action space.

## Slide 9: Analytical Benchmark: FHPD Network
Fixed Hopping Pattern Dynamics: PUs switch channels in a structured way.
Allows derivation of optimal sensing & access policy.
Benchmark helps validate DDQSA performance.

## Slide 10: Key Theoretical Results
1. SU can infer full network state with finite history.
2. Optimal access: choose channel with highest transition probability.
3. DDQSA achieves near-optimal throughput in benchmark scenarios.

## Slide 11: Simulation Setup
Parameters: N=10 channels, L=5 sensed channels, H=6 history length.
Training with replay buffer and ε-decay.
- replay buffer are used to store past transitions . It samples mini-batches randomly during training.
Comparison with baseline strategies: Random Access, Random Sensing, Alternating Sensing.

## Slide 12: Performance Comparison
DDQSA outperforms all baselines across various PU traffic models.
Achieves near-optimal throughput with narrowband sensing.
Better adapts to SU idle times and uncertain sensing.

## Slide 13: Main Contributions
Joint optimization of sensing and access using DRL.
First to apply DDQN for simultaneous learning.
Supports uncertain sensing and idle SU behavior.
Demonstrates scalable and distributed implementation.

## Slide 14: Conclusion
DDQSA enables efficient spectrum access with partial observations.
Performs well in both analytical and simulated benchmarks.
Future work: multi-user extension, real-world implementation.