## Slide 1: SINR-Aware DRL for Distributed DCA in Cognitive Interference Networks

## Slide 2: Introduction
• Dynamic Channel Allocation (DCA) adapts frequency use in real-time to optimize spectrum utilization.
• SINR (Signal-to-Interference-plus-Noise Ratio) is a key metric indicating communication quality.
• Cognitive Radio Networks face challenges from spectrum scarcity and interference.

## Slide 3: Motivation
Traditional models assume orthogonal channels—unrealistic in dense environments.
Inter-Carrier Interference (ICI) and channel reuse increase problem complexity.
Need for scalable, distributed algorithms that adapt to real-world dynamics.

## Slide 4: System Model
• N networks, each with Mₙ users.
• K overlapping channels, reused by multiple networks.
• Orthogonality is not preserved—ICI is present.
• SINR calculated per user per channel considering path loss and interference.

## Slide 5: SINR Model
Non-orthogonal channel allocation → Inter-Carrier Interference (ICI)
SINR computed per user per channel, considering interference from other networks
SINR Equation: SINR = PR / (IT + I), where PR is received power, IT is noise, I is interference
Received Power: PR = PT - PL, PL using Egli path loss model
Egli Path Loss: PL = 40log(d) - 20log(40/f) - 20log(H_T H_R) - 10log(G_T G_R) d = Euclidean distance
Interference Power summed over users from other networks and their channels
Spectral Attenuation increases with frequency distance |k - k'|
Thermal Noise: IT = 10log(kB·T·B·NF) + 30 [dBm]

## Slide 6: Problem Formulation
Objective:
Maximize average SINR per network:
max Σ SINRₙ_cₙ subject to SINRₙ_cₙ ≥ SINR* for all n
. SINR*: QoS threshold
. cₙ: Chosen channel for network n

## Slide 7: CARLTON Training Procedure
Centralized Training with Decentralized Execution (CTDE).
Uses DeepMellow: stable Q-learning without a target network.
Input: Concatenation of channel binary rep (previous action) and QVₙ.
Action selection via Mellowmax and action masking (if QVₙ[k]=0, set Q-value to -∞).
Reward backprop via Huber Loss.
Replay memory and batch updates across scenarios.

## Slide 8: Observation Space
Each user in a network sends a vector of SINR values for all K channels.
These vectors are aggregated into an Mₙ × K matrix.
A binary matrix BSINRₙ is derived:
BSINRₙ[j,k] = 1 if SINRₙ[j,k] > SINR*, else 0
Averaging across users gives Quality Vector QVₙ ∈ ℝᴷ.
QVₙ is the key observation used by agents.

## Slide 9: Action & Reward Space
• Action: an(t) ∈ {1,...,K}, i.e., select one channel.
• Reward:
r = ρ·rₚ + (1-ρ)·r_sw
- rₚ: personal reward based on channel quality QVₙ and action stability
- r_sw: social welfare reward, averaging rₚ of nearby networks
ρ balances selfish vs cooperative learning.

## Slide 10: Key Training Equations
Action Selection
Pr(aₙ(t)=k) ∝ (1-α)·e^{β·Q(s,k)} + α/K
- Helps each network or agent select a channel in a probabilistic but Q-informed way.
-Provides exploration (α\alphaα) and exploitation (via Q(s,k) balance
Huber Loss:
Lδ(e) = ½e² if |e|≤δ, else δ(|e| - ½δ)
- loss that behaves like squared error for small errors, and absolute error for large errors.
Mellowmax target value smoothing:
eₙ = rₙ(t) + γ·mm_ω(Q(s',·)) - Q(s,a)
Mellowmaxω​(Q(s,⋅))=1/ωlog(1/∣A∣​∑​eωQ(s,a))
Final reward:
-> r = ρ·rₚ + (1−ρ)·r_sw

## Slide 11: Simulation Environment
Each network has 2–22 users distributed in 2D space.
Channels: 10 overlapping, 2MHz apart, non-orthogonal.
SINR computed via Egli model for realistic path loss.
Thermal noise IT = -104.9 dBm with control channel overhead.
Evaluation: mean/median CQ, convergence time, spectrum efficiency.

## Slide 12: Evaluation Metrics
Channel Quality (CQ): average QoS satisfaction across users.
ANCCS: Avg. Number of Channel Changes Score = 1 - ANCC/T
CTS: Convergence Time Score = 1 - CT / (T·N)
- Measures how quickly the system converges to a stable channel allocation.
SES: Spectrum Efficiency Score from QVₙ smoothness.
WS: Weighted Score: 0.4·CQ + 0.1·ANCCS + 0.4·CTS + 0.1·SES

## Slide 13: Performance of CARLTON
CARLTON outperforms:
- Random Agent (RA)
- Jamming Avoidance Response (JAR)
45% better than RA, 20% better than JAR on average WS.
Within 2.5% of centralized graph-coloring (optimal).
Maintains minCQ > 0.95 even with 15 networks .

## Slide 14: Social Reward Sensitivity
ρ tunes cooperation:
- Low ρ → fairness, cooperation
- High ρ → fast convergence
Γ = 500m optimal for neighbor consideration.
Trade-off between convergence and spectrum mobility.
- Increasing ρ or shrinking Γ may speed up learning, but may lead to poor adaptation.

## Slide 15: Conclusion
• CARLTON enables distributed, scalable channel allocation in realistic networks.
• Handles interference, partial observability, and non-orthogonality.
• Outperforms alternatives while achieving near-centralized results.
• Future work: extend to 3D mobility, integrate other RL models.